## Slide 1: UVM Verification Summary

## Slide 2: UVM is:
a method for functional verification using SystemVerilog, complete with a supporting library of SystemVerilog code.
Universal Verification Methodology
created by Accellera based on the OVM (Open Verification Method) version 2.1.1. The roots of these methods lie in the application of the languages IEEE 1800™ SystemVerilog, IEEE 1666™ SystemC, and IEEE 1647™ e.

## Slide 3: UVM testbenches
replace SystemVerilog framework and coding style for testbenches.
are more than traditional HDL testbenches, which wiggle pins on the DUT and rely on the designer to inspect a waveform diagram to verify correct operation.
are complete verification environments composed of reusable verification components, and used as part of an overarching method of constrained random, coverage-driven, verification.

## Slide 4: Verification Done Right
Start with a statement of the function of the DUT.
From this, derive a verification plan
  feature-by-feature
  agreed in advance by all those on team
  basis for the whole verification process.
Verification complete?
  Every item on the plan tested to an acceptable level?

## Slide 5: Random Thoughts
1) simple non-random tests to bring up the design
2) fully random tests explore the state space broadly and flush out as many bugs as possible with minimum test writing effort.
3) Defining a series of tests which constrain/shape the random stimulus is a different way to push the design into interesting corner cases.
  Constrained random stimulus = compromise between 1 and 2, but effective usage requires good engineering judgement: use the priorities set in the verification plan to direct verification resources to the key areas.

## Slide 6: Checkers, Coverage, and Constraints, Oh My!
Checkers ensure functional correctness.
  implemented using SystemVerilog assertions or using regular procedural code.
  assertions can be embedded within the design-under-test, placed on the external interfaces, or can be part of the verification environment.
  UVM provides mechanisms and guidelines for building checkers into the verification environment and for logging reports.

## Slide 7: Coverage
Measures the functional completeness of the testing
  tells when you've met the goals in the verification plan
SystemVerilog has:
  property-based coverage (cover directives)
  sample-based coverage (covergroups)
Both work in UVM
specification of the coverage model is tied to the verification plan, and many simulation tools are able to annotate coverage information onto the verification plan document, facilitating tight management control.

## Slide 8: Constraints
Help reach coverage goals by shaping the random stimulus to push the design-under-test into interesting corner cases.
SystemVerilog can express constraints
UVM provides mechanisms that allow constraints to be written as part of a test rather then embedded within dedicated verification components.
This and other features of UVM facilitate the creating of reusable verification components.

## Slide 9: Verification Reuse
UVM facilitates the construction of verification environments and tests by providing:
  reusable machinery in a library of SystemVerilog classes
  set of guidelines for best practice for SystemVerilog for verification.
UVM enhances verification productivity through component reuse
  modular verification environment
  each component has clearly defined responsibilities
  flexibile configuration and use
  allow customization of imported components
  well-defined coding guidelines to ensure consistency.