## Slide 1: UVM Basis
Adapted from ARM Lecture
Nagesh Loke

## Slide 2: Challenges of verifying complex systems
Processor development can take 100s of engineering years
Requires parallel developments across multiple sites
  need large team to verify a processor
Typical method: divide and conquer, partition CPU into smaller units and verify them, then reuse checkers and stimului at a higher level
Reuse code to avoid duplication of work
integrate external IP
This requires rigorous planning, code structure, lockstep development, and standardization

## Slide 3: Universal Verification Method
Benefits:
  supports and provides framework for modular and layered verification components
  Enables:
    reuse
    clear functional definition for each component
    configuration of components to be used in a variety of contexts
maintained by Accellera committee
Fully open source code
training and support available

## Slide 4: UVM Test Bench

## Slide 5: UVM Sequence & Genealogy

## Slide 6: UVM Component
Building block of components that control testbench or transactions
Have time-consuming run() task
Exist for life of test

## Slide 7: push_driver vs. driver??
push_driver waits until sequencer pushes a transaction into its port
  Never initiates a transaction
  Passively does what the sequencer tells it to
  Rarely used, mainly for OVM backward compatibility
driver requests items to execute
  Executes upon receipt
  Tells sequencer when done, requests new item
  Takes initiative

## Slide 8: Sequence
Sequence item = transaction
Examples: packet, AXI transaction, pixel
Sequence = lit of sequence items
Sequence can be separated into a generator

## Slide 9: Sequencer vs Sequence
Sequencer sends transaction from sequence to driver
Sends driver response back to sequence
Can arbitrate among sequences (Salemi Ch 23)
Methods: send_request(), get_response()
Driver decodes transaction from sequencer
Drives DUT interface sinals
Pin-level protocol and timing relationships
(Here, cb probably denotes clocking block)

## Slide 10: Monitor
Observes communications
Can check pin protocols
Creates transactions based on interface activity
Communicates using analysis ports

## Slide 11: Agent
Connects sequencer, driver, monitor
Provides analysis ports
monitor to scoreboard & coverage
Can disable sequencer & driver

## Slide 12: Scoreboard
Accepts transactions from monitors
Applies inputs to independent model & generates expected output
Compares actual vs. expected outputs
Queue of modeled outputs
  Pops latest result when DUT output is available
Manages timing of inputs vs. outputs

## Slide 13: Environment
Manages components in testbench
Instantiates & connects:
agents
scoreboards
coverage modules

## Slide 14: UVM Test
Creates environment
Controls types of tests to run
Configures components

## Slide 15: TLM port
Mechanism to transport data or messages
SystemVerilog mailbox
Carries transaction
Analysis port for broadcast (one  many branching)
TLM port makes component more modular & reusable

## Slide 16: Phasing
Create components, allocate memory
Hook up (plumbing)
Print banners, topology, etc.
End checks (objections dropped)
Report, pass/fail status
Complete test
Reset DUT
Configure desigh
Run tests
Halt stimulus; drain transactions